# CS9100 Navigation Box RGB Cable

# Pinout

| RGB socket | Wire purpose | Wire colour | Symbol on the label |
| --- | --- | --- | --- |
| 1 | RGB Red (video signal) | Red | R |
| 2 | RGB Green (video signal) | Green | G |
| 3 | RGB GND (video signal) | Black | GND |
| 4 | RGB Sync (video signal) | Yellow | SYNC |
| 5 | RGB Blue (video signal) | Blue | B |
| 6 | Control | White | IR DATA |
| 7 | Service power +12 V | Red, thick | VCC |
| 8 | Right channel (audio signal) | Brown | AUDIO R |
| 9 | Left channel (audio signal) | Orange | AUDIO L |
| Connector shield | Ground (audio signal) | Armour | ----------- |