CS9100 Navigation Box Connection to

JVC Multimedia Receivers by the example of

KW-AVX836/KW-AVX835/KW-AVX736/KW-AVX735

In order to avoid breakdown CS9100 navigation box should be connected to JVC multimedia receiver while power off.

CS9100 Setting Up

It is necessary to activate the corresponding protocol before CS9100(RV) connection to JVC multimedia receiver.  Otherwise, image will not be displayed on the JVC receiver screen. To do this, power on the navigation box and connect it to TV set or any other video signal receiver via composite output. After that use remote control unit to select “Settings” menu item, in new window select “System Config” (fig. 1), move to “Panel I” tab and select “JVC” protocol (fig. 2). Press SAVE button. After protocol is activated select “Calibration” menu item (fig. 1) and using PDA stylus or any other not sharp stick perform JVC touch screen display calibration according to CS9100(RV).

Figure 1

Figure 2

JVC Receiver Setting Up

When CS9100(RV) navigation box is connected to JVC multimedia receiver and on-board power supply you can proceed to setting up the receiver (fig. 3).

Figure 3

CS9100 Image Activation

In order to activate image from CS9100(RV) navigation box you should press DISP button a couple of times (fig. 4), until image from CS9100(RV) navigation box appears.

Figure 4

Connection Diagram